## Slide 1: Basic Switch and Router Configuration

## Slide 2: Access Methods
Console – A physical management port used to access a device in order to provide maintenance, such as performing the initial configurations.
Secure Shell (SSH) – Establishes a secure remote CLI connection to a device, through a virtual interface, over a network. (Note: This is the recommended method for remotely connecting to a device.)
Telnet – Establishes an insecure remote CLI connection to a device over the network. (Note: User authentication, passwords and commands are sent over the network in plaintext.)

## Slide 3: IOS Navigation Primary Command Modes
User EXEC Mode:
  Allows access to only a limited number of basic monitoring commands
  Identified by the CLI prompt that ends with the > symbol
Privileged EXEC Mode:
  Allows access to all commands and features
  Identified by the CLI prompt that ends with the # symbol
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.1 – Primary Command Modes

## Slide 4: IOS Navigation Configuration Mode and Subconfiguration Modes
Global Configuration Mode:
  Used to access configuration options on the device
Line Configuration Mode:
  Used to configure console, SSH, Telnet or AUX access
Interface Configuration Mode:
  Used to configure a switch port or router interface
Notes: 2 – Basic Switch and End Device Configuration
2.2 – IOS Navigation
2.2.2 – Configuration Mode and Subconfiguration Modes

## Slide 5: Basic Device Configuration Device Names
The first configuration command on any device should be to give it a unique hostname.
By default, all devices are assigned a factory default name. For example, a Cisco IOS switch is "Switch.”
Guideline for naming devices:
    Start with a letter
    Contain no spaces
    End with a letter or digit
    Use only letters, digits, and dashes
    Be less than 64 characters in length
Note: To return the switch to the default prompt, use the no hostname global config command.
Notes: 2 – Basic Switch and End Device Configuration
2.4 – Basic Device Configuration
2.4.1 – Device Names

## Slide 6: Basic Device Configuration Password Guidelines
The use of weak or easily guessed passwords are a security concern.
All networking devices should limit administrative access by securing privileged EXEC, user EXEC, and remote Telnet access with passwords. In addition, all passwords should be encrypted and legal notifications provided.
Password Guidelines:
    Use passwords that are more than eight characters in length.
    Use a combination of upper and lowercase letters, numbers, special characters, and/or numeric sequences.
    Avoid using the same password for all devices.
    Do not use common words because they are easily guessed.
Note: Most of the labs in this course use simple passwords such as cisco or class. These passwords are considered weak and easily guessable and should be avoided in production environments.
Notes: 2 – Basic Switch and End Device Configuration
2.4 – Basic Device Configuration
2.4.2 – Password Guidelines

## Slide 7: Basic Device Configuration Configure Passwords
Securing user EXEC mode access:
    First enter line console configuration mode using the line console 0 command in global configuration mode.
    Next, specify the user EXEC mode password using the password password command.
    Finally, enable user EXEC access using the login command.
Securing privileged EXEC mode access:
    First enter global configuration mode.
    Next, use the enable secret password command.
Notes: 2 – Basic Switch and End Device Configuration
2.4 – Basic Device Configuration
2.4.3 – Configure Passwords

## Slide 8: Basic Device Configuration Configure Passwords (Cont.)
Securing VTY line access:
    First enter line VTY configuration mode using the line vty 0 15 command in global configuration mode.
    Next, specify the VTY password using the password password command.
    Finally, enable VTY access using the login command.
Note: VTY lines enable remote access using Telnet or SSH to the device. Many Cisco switches support up to 16 VTY lines that are numbered 0 to 15.
Notes: 2 – Basic Switch and End Device Configuration
2.4 – Basic Device Configuration
2.4.3 – Configure Passwords

## Slide 9: Basic Device Configuration Encrypt Passwords
The startup-config and running-config files display most passwords in plaintext.
To encrypt all plaintext passwords, use the service password-encryption global config command.
Use the show running-config command to verify that the passwords on the device are now encrypted.
Notes: 2 – Basic Switch and End Device Configuration
2.4 – Basic Device Configuration
2.4.4 – Encrypt Passwords

## Slide 10: Basic Device Configuration Banner Messages
A banner message is important to warn unauthorized personnel from attempting to access the device.
To create a banner message of the day on a network device, use the banner motd # the message of the day # global config command.
Note: The “#” in the command syntax is called the delimiting character. It is entered before and after the message.
The banner will be displayed on attempts to access the device.
Notes: 2 – Basic Switch and End Device Configuration
2.4 – Basic Device Configuration
2.4.5 – Banner Messages

## Slide 11: Secure Remote Access Telnet Operation
Telnet uses TCP port 23. It is an older protocol that uses unsecure plaintext transmission of both the login authentication (username and password) and the data transmitted between the communicating devices.
A threat actor can monitor packets using Wireshark. For example, in the figure the threat actor captured the username admin and password ccna from a Telnet session.
Notes: 1 – Basic Device Configuration
1.3 – Secure Remote Access
1.3.1 – Telnet Operation

## Slide 12: Secure Remote Access SSH Operation
Secure Shell (SSH) is a secure protocol that uses TCP port 22. It provides a secure (encrypted) management connection to a remote device. SSH should replace Telnet for management connections. SSH provides security for remote connections by providing strong encryption when a device is authenticated (username and password) and also for the transmitted data between the communicating devices.
The figure shows a Wireshark capture of an SSH session. The threat actor can track the session using the IP address of the administrator device. However, unlike Telnet, with SSH the username and password are encrypted.
Notes: 1 – Basic Device Configuration
1.3 – Secure Remote Access
1.3.2 – SSH Operation

## Slide 13: Secure Remote Access Verify the Switch Supports SSH
To enable SSH on a Catalyst 2960 switch, the switch must be using a version of the IOS software including cryptographic (encrypted) features and capabilities. Use the show version command on the switch to see which IOS the switch is currently running. An IOS filename that includes the combination “k9” supports cryptographic (encrypted) features and capabilities.
The example shows the output of the show version command.
Notes: 1 – Basic Device Configuration
1.3 – Secure Remote Access
1.3.3 – Verify the Switch Supports SSH

## Slide 14: Configure a Switch with Initial Settings Switch SVI Configuration Example (Cont.)
Task | IOS Commands
Enter global configuration mode. | S1# configure terminal
Enter interface configuration mode for the SVI. | S1(config)# interface vlan 1
Configure the management interface IPv4 address. | S1(config-if)# ip address 172.17.99.11 255.255.255.0
Enable the management interface. | S1(config-if)# no shutdown
Return to the privileged EXEC mode. | S1(config-if)# end
Save the running config to the startup config. | S1# copy running-config startup-config
Notes: 1 – Basic Device Configuration
1.1. – Configure a Switch with Initial Settings
1.1.6 – Switch SVI Configuration Example (Cont.)

## Slide 15: Configure a Switch with Initial Settings Switch SVI Configuration Example (Cont.)
Step 2: Configure the Default Gateway
The switch should be configured with a default gateway if it will be managed remotely from networks that are not directly connected.
Task | IOS Commands
Enter global configuration mode. | S1# configure terminal
Configure the default gateway for the switch. | S1(config)# ip default-gateway 172.17.99.1
Return to the privileged EXEC mode. | S1(config-if)# end
Save the running config to the startup config. | S1# copy running-config startup-config
Notes: 1 – Basic Device Configuration
1.1. – Configure a Switch with Initial Settings
1.1.6 – Switch SVI Configuration Example (Cont.)

## Slide 16: Secure Remote Access Configure SSH
Before configuring SSH, the switch must be minimally configured with a unique hostname and the correct network connectivity settings.
  Step 1: Verify SSH support - Use the show ip ssh command to verify that the switch supports SSH. If the switch is not running an IOS that supports cryptographic features, this command is unrecognized.
  Step 2: Configure the IP domain - Configure the IP domain name of the network using the ip domain-name domain-name global configuration mode command.
  Step 3: Generate RSA key pairs - Generating an RSA key pair automatically enables SSH. Use the crypto key generate rsa global configuration mode command to enable the SSH server on the switch and generate an RSA key pair.
  Step 4: Configure user authentication - The SSH server can authenticate users locally or using an authentication server. To use the local authentication method, create a username and password pair using the username username secret password global configuration mode command.
  Step 5: Configure the vty lines - Enable the SSH protocol on the vty lines by using the transport input ssh line configuration mode command. Use the line vty global configuration mode command and then the login local line configuration mode command to require local authentication for SSH connections from the local username database.
  Step 6: Enable SSH version 2 - By default, SSH supports both versions 1 and 2. When supporting both versions, this is shown in the show ip ssh output as supporting version 2. Enable SSH version using the ip ssh version 2 global configuration command.
Notes: 1 – Basic Device Configuration
1.3 – Secure Remote Access
1.3.4 – Configure SSH

## Slide 17: Secure Remote Access Verify SSH is Operational (Cont.)
To display the version and configuration data for SSH on the device that you configured as an SSH server, use the show ip ssh command. In the example, SSH version 2 is enabled.
Notes: 1 – Basic Device Configuration
1.3 – Secure Remote Access
1.3.5 – Verify SSH is Operational (Cont.)